## Slide 1: INTRODUCTION TO WIRELESS SENSOR NETWORKS
CHAPTER 7: TIME SYNCHRONIZATION
Anna Förster

## Slide 2: OVERVIEW
Clocks and Delay Sources
Requirements and Challenges
Time Synchronization Protocols
  Lightweight Tree Synchronization
  Reference Broadcast Synchronization
  NoTime

## Slide 3: Clocks and Delay Sources
Clock resolution or rate is the step at which the clock progresses and can be read
Clock skew or drift is the difference between the progressing speeds of two clocks
Clock offset is the difference between the time shown by two different clocks
Clock jitter is when the individual ticks of a clock are not perfectly the same

## Slide 4: Requirements and Challenges (1)
Two clocks drift apart even after synchronization
The maximum drift rate of a clock dictates the synchronization period where ρ is the maximum drift rate in ppm (parts per million), δ is the maximum allowed drift in seconds and τsync is your needed synchronization period.

## Slide 5: Requirements and Challenges (2)
The time synchronization protocol cannot jump back and forth in time.
Time synchronization accuracy is the maximum offset between the synchronized clock and a reference clock (for example global time).
Time synchronization precision is the maximum offset between any two synchronized clocks.
Time synchronization precision is important to understand the sensor data.

## Slide 6: Understanding Sensor Data

## Slide 7: Time Synchronization Protocols
Externally Synchronized: there is an external source of correct time data.
Internally Synchronized: consistent view from all nodes, but not globally correct time.

## Slide 8: Sender-Receiver Synchronization
Long critical path

## Slide 9: Receiver-Receiver Synchronization
Shorter critical path

## Slide 10: Lightweight Tree Synchronization (LTS)
Build a spanning tree from root (sink) to all nodes
Sink has globally correct time
Sink sends a message to its children to sync them, then traverse the tree
Use sender-receiver synchronization
Precision depends on depth of tree and does not scale

## Slide 11: Reference Broadcast Synchronization (RBS)
Uses receiver-receiver synchronization
Broadcast correct time to all neighbors
Total precision increases with number of broadcasts
Scales well
Not very efficient in terms of communication overhead

## Slide 12: NoTime Protocol
Do not try to time sync the nodes directly
Provide enough information so that the sink can reconstruct the real time
Save delays on the way
Precision depends on:
  Propagation Delay
  Hardware Delay
  Local time resolution

## Slide 13: SUMMARY
Clock skew causes two clocks to progress at different rates, while clock jitter causes a clock to tick irregularly.
Provide efficiency and simplicity:
  Regular synchronization is needed.
  Available time cannot jump back and forth in.
Lightweight tree synchronization protocol (LTS) uses the sender-receiver synchronization message exchange and is not scalable.
Broadcast reference protocol (RBS) uses the receiver-receiver synchronization message exchange, has greater precision than LTS and is scalable.
NoTime does not synchronize the nodes, but computes the in-network delay for each data packet, which enables the sink to compute the original event’s real time.