## Slide 1: INTRODUCTION TO WIRELESS SENSOR NETWORKS
CHAPTER 2: ANATOMY OF A SENSOR NODE
Anna Förster

## Slide 2: INTRODUCTION TO WIRELESS SENSOR NETWORKS
CHAPTER 1: WHAT ARE WIRELESS SENSOR NETWORKS?
Anna Förster

## Slide 3: OVERVIEW
Hardware components
Power Consumption
Operating Systems and Concepts
  Memory Management
  Interrupts
  Tasks, Threads and Events
Simulators
Communication Stack

## Slide 4: HARDWARE COMPONENTS
Microcontroller
Radio transceiver
Sensor
External memory
Battery
Serial adapter
Embedded antenna
Oscillator
Z1 sensor node.
Notes: Use the test of the section to explain what is what and what the individual components do.

## Slide 5: POWER CONSUMPTION
Sensor nodes operate on batteries
Each component on the sensor node consumes power
  Measured in Ampere (A, current) or milli Ampere (mA).
Power consumption of Z1 sensor nodes

## Slide 6: EXERCISE: BATTERIES
Explore the batteries in front of you.
What is their nominal capacity?
Consider a scenario, where the sensor node is working in cycles. Every cycle, the components are working with the following time percentages:
  Radio: 10% send, 10% receive, 80% sleep
  Microcontroller: 10% active, 90% sleep
  Temperature sensor: 5% sense, 95% sleep
  The other components are always sleeping /inactive.
Compute the energy consumption of one cycle with length 1 second.
Now assume the active time of all components is halved. What is now the energy consumption of 1 cycle of length 1 second?
For both scenarios above, compute the theoretical lifetime of the sensor nodes, considering the battery capacity in front of you.
Discuss your results.
Notes: Let the students first read the explanation of the nominal capacity of batteries on page 13. Prepare beforehand AA batteries of different types and distribute in the class (groups of 2 students are better for cooperation). The parameters above can be easily changed. It is also a good idea to let different groups compute different scenarios and then let them present their results to the other students and discuss.

## Slide 7: CONCEPTS OF OPERATING SYSTEMS
The tasks of the operating system:
Manage software and hardware
Allow the user to access easily the hardware
Allow several programs to run simultaneously
Manage the memory of the system
Manage shared resources (memory, CPU, external devices)

## Slide 8: Memory Management
Static memory management: Reserve all memory at compilation time.
  Simple, does not need have any overhead for management
  Inflexible, cannot extend on demand
Dynamic memory management: A special memory management software reserves memory on demand.
  Flexible, uses only memory which is really needed
  Complex to maintain, can easily overflow on memory-restricted devices (like sensor nodes)

## Slide 9: EXERCISE: MANAGE MEMORY
Read Section “Memory Management Example” on page 19.
Discuss the usage of the Big-O Notation.
Explain the different implementations and compare against each other.
Do you have other ideas of how to implement the same functionality?

## Slide 10: INTERRUPTS
Goal: react as fast as possible to an external signal (sensor, user, etc.)
Example: ask sensor for data.
Problem: sensor does not answer immediately.

## Slide 11: TASKS
Interrupts are used to control the flow of programs
How to enable several programs to run simultaneously?
Task: an independent process in the system with its own resources and memory, which works independently from all other processes
Memory management unit: makes sure memory is allocated to each process and that processes cannot access/corrupt memory of other processes.
Multitasking: the scheduler decides which task is allowed to proceed and which is interrupted.
Shared resources: the process needs access to some shared resource/device, e.g. printer or network interface. This access should not be interrupted.
Atomic operations: runs until completion and nobody can interrupt it.
DISADVANTAGE: tasks are resource-intensive

## Slide 12: EVENT BASED PROGRAMMING
An alternative to multi-tasking
Based on events as opposed to interrupts: events are not necessarily handled immediately (like interrupts) and can be generated also by software components. For example, a lengthy processing job can create intermediate results and signal those by creating events.
Each event correspond to one or more event handlers, which process the event.
Event-based programming is based on finite state machines.
QUESTION: what is a finite state machine?
DISADVANTGE: Finite state machines are not trivial to implement and do not scale well.

## Slide 13: EXERCISE: PROTOTHREADS
Inform yourself on the Contiki website about protothreads.
Implement a small application, which uses protothreads
Discuss the usage of protothreads in terms of technical efficiency and ease of implementation

## Slide 14: SIMULATORS
A software system, running on a normal computer, which mimics the behavior of some other system and its interactions
Various tools exist:
  Cooja for the Contiki operating system
  OMNeT++ for more sophisticated and general-purpose network simulators
  Many others

## Slide 15: SIMULATION MODELS
Simulation relies on simulation models, which mimic the behavior of individual real components and properties
Wireless propagation models: how does the wireless signal propagates through different environments?
Mobility models: how do the mobile nodes move around?
Energy expenditure models: how much energy is needed for individual components and/or tasks?
Traffic model: how much data is sent and when?

## Slide 16: COMMUNICATION STACK
Reduced sensor network communication stack (as opposed to OSI)

## Slide 17: PROTOCOLS VS. ALGORITHMS
Algorithm: a general-purpose, parameter-based computation flow.
Protocol: exact implementation of one or more stack layers, parameters are often fixed or a very limited number of options is provided

## Slide 18: SUMMARY
Sensor node consists of microcontroller, radio transceiver, sensors, serial connection, LEDs, flash memory.
Each component needs energy, with radio and flash being the most “hungry” ones.
Putting individual components to sleep saves energy.
Towards the end of battery lifetime, performance of individual components degrades and might deliver false results.
WSN operating systems are simple and usually have only limited dynamic memory and multi-tasking functionalities.