## Slide 1: INTRODUCTION TO WIRELESS SENSOR NETWORKS
CHAPTER 3: RADIO COMMUNICATIONS
Anna Förster

## Slide 2: OVERVIEW
Radio Waves and Modulation/Demodulation
Properties of Wireless Communications
  Interference and noise
  Hidden Terminal Problem
  Exposed Terminal Problem
Medium Access Protocols
  Design Criteria for Medium Access Protocols
  Time Division Multiple Access
  Carrier Sense Multiple Access
  Sensor MAC
  Berkeley MAC
  Optimizations of B-MAC
  Other Protocols and Trends

## Slide 3: RADIO WAVES

## Slide 4: RADIO WAVES

## Slide 5: MODULATION/DEMODULATION
Waves do not carry information by themselves.
By changing one or more of the parameters of a wave, we can encode information into it.
Signal modulation/demodulation. This is the process of changing radio wave parameters in a well-defined way to encode/decode information into/from the wave.

## Slide 6: AMPLITUDE MODULATION
Amplitude A(t): This parameter gives how high the wave is. To encode information, you can change the amplitude from very small (encoding a 0) to very high (encoding a 1).

## Slide 7: FREQUENCY MODULATION
Frequency or period f(t). This parameter dictates how often the wave form is repeated over time. The frequency of the signal can be changed to indicate different codes.

## Slide 8: PHASE MODULATION
Displacement or phase 𝜙(t). This parameter identifies the displacement of the wave in respect to the beginning of the axes. You can displace the wave to indicate change of codes.

## Slide 9: Properties of Wireless Communications
While traveling through the environment (we talk about wave propagation), the electromagnetic wave experiences multiple distortions:
Attenuation
Reflection/Refraction
Diffraction/Distortion
Doppler Effect

## Slide 10: Attenuation
This process spreads the energy of the wave to larger space. It is similar to a balloon, which is a dark red color before filling it with air, but then becomes almost transparent once filled. Thus, with growing distance from the sender, the wave becomes less and less powerful and harder to detect

## Slide 11: Reflection / Refraction
This process changes the direction of the wave when it meets a surface. Part of the wave gets reflected and travels a new trajectory, another part of the wave gets refracted into the material and changes its proper- ties. Both processes create new, secondary waves, which also reach the receiver at some point in time, slightly after the primary wave.

## Slide 12: Diffraction / Scattering
Sharp edges and uneven surfaces in the environment can break the wave into several secondary waves

## Slide 13: Doppler Effect
The frequency of the signal changes with its relative velocity to the receiver. The Doppler effect is well known for its impact on the police siren, which sounds different to the observer depending on whether the police car is approaching or moving away. The same happens with the radio waves when their frequencies get shifted in one or the other direction which results in a loss of center.

## Slide 14: Path Loss
Path loss is the reduction in power density of an electromagnetic wave as it propagates through space.
All these properties lead to:

## Slide 15: Interference
Electromagnetic interference is the disturbance of an electromagnetic signal due to an external source. It is typically measured with the signal-to-interference ratio (SIR) or with signal-to-noise plus interference ratio (SNIR).
Caused by:
Other sensor networks
Bluetooth
WiFi
Microwaves, etc.

## Slide 16: Noise
Electromagnetic noise is the unwanted fluctuation of a signal or energy from natural sources such as the sun. It is generally distinguished from interference or from systematic alteration of the signal such as in the Doppler Effect. It is typically measured with signal-to-noise ratio (SNR) to identify the strength of the useful signal compared to the overall environmental noise.

## Slide 17: Hidden Terminal Problem
Collision at Node B! A is hidden from C.

## Slide 18: Exposed Terminal Problem
B and C could send their data simultaneously, but believe to interfere with each other.

## Slide 19: Medium Access Protocol (MAC)
The role of Medium Access Protocols is to regulate the access of the sensor nodes to the shared wireless medium, this is, to the “air”
Metrics used to optimize its behavior:
  Throughput: number of bits or bytes successfully transmitted per time unit
  Delay: amount of time between sending a packet and receiving the packet
The main goal of medium access protocols is to prevent interference and corrupted packets, while maximizing the throughput of the wireless medium and minimizing the energy spent.

## Slide 20: Design Criteria for MAC Protocols
Minimize Collisions
Minimize Overhearing
Minimize Idle Listening
Minimize Overhead
No single optimal solution, always a tradeoff!

## Slide 21: Time Division Multiple Access (TDMA)
Organize communications in a network is by time
Divide the time available across the nodes into slots and give the nodes full control over their slots

## Slide 22: General TDMA Algorithm

## Slide 23: Centralized TDMA
Schedule is calculated offline:
  If no information about topology is known, then reserve N slots for N nodes.
    PRO: simple and robust
    CON: slow
  With additional information available, reuse as many slots as possible to minimize duration of rounds.
    PRO: faster
    CON: very sensitive to changes in the network
Provided to sensor nodes at startup

## Slide 24: Distributed TDMA
Nodes attempt to find a good schedule by cooperation
Start by competing for access (all together)
Exchange neighbor information in terms of link quality
Compete for the slots by trying to reserve them then release them again if interference occurs
PRO: Efficient and does not need a central decision point
CON: Initialization long and needs to be repeated in case of changes

## Slide 25: Discussion of TDMA
Not efficient in case of very low traffic
Nodes with more traffic do not get more slots
In multi-hop networks, TDMA schedule affects greatly end-to-end delay:

## Slide 26: Carrier Sense Multiple Access (CSMA)
“Listen before Talk”
Listen to channel first
If free, send
If not, re-try later
Two main variants:
  CSMA-CA: with collision avoidance (used more often)
  CSMA-CD: with collision detection

## Slide 27: CSMA-CA General Algorithm

## Slide 28: RTS/CTS Handshake
Ready-to-send, clear-to-send short messages
Designed to avoid the hidden terminal problem

## Slide 29: RTS/CTS in Hidden Terminal
Successfully solves the problem:

## Slide 30: RTS/CTS - Problems
Another problematic case:

## Slide 31: Variants of CSMA
1-persistent CSMA
Non persistent CSMA
P-persistent CSMA (implemented in IEEE802.15.4, lower layer of Zigbee)
O-persistent CSMA

## Slide 32: Sensor Node Duty Cycle
Duty cycle is the relation between the length of the active and sleeping cycles of a sensor node and is measured in percent. It is defined as:

## Slide 33: Sensor MAC (S-MAC)
Especially designed to enable low duty cycles
Nodes communicate only during their active cycles
How to synchronize the nodes’ active cycles?
  At startup, a node listens first to receive a schedule from a neighbor
  If none received, start your own schedule
  Every active cycle, send your own schedule
Results in synchronized islands, where bridge nodes need more power to support two schedules
Needs a time synchronization protocol (Chapter 7)

## Slide 34: S-MAC General Scenario

## Slide 35: Timeout MAC (T-MAC)
S-MAC wastes a lot of energy with very low traffic, as the nodes stay awake during the complete active cycle
Timeout-MAC solves this problem:
  At active cycle and no traffic, go back to sleep.

## Slide 36: Berkeley MAC (B-MAC)
Tackles the problems of S-MAC
Does not need time synchronization
Solution: Long preambles
A preamble is a special communication message of varying lengths, which does not carry any application data or other payloads. Instead, it signals to neighbors that a real message is waiting for transmission. The preamble can carry sender, receiver, and packet size information or other administrative data to simplify the communication process.

## Slide 37: B-MAC General Scenario

## Slide 38: Optimizations of B-MAC
X-MAC: Interrupt the preamble sender, when the receiver is awake
  Minimize the idling time of sender and receiver
  Only for unicast transmissions
Box-MAC: Considered an implementation of X-MAC with clearly defined parameters
Tackle broadcast transmissions:
  Avoid the preamble sending, send repeatedly the data itself
  Inform the receivers when the data will be send, so they can go to sleep

## Slide 39: IEEE 802.15.4
CSMA-CA based protocols
Operates on free-license channels
  868/915 MHz
  2450 MHz
S-MAC, B-MAC, X-MAC work on top of it
Basis for many standards:
  Zigbee
  WirelessHART
  ISA100
  and many more

## Slide 40: Summary (1)
Main properties of wireless communications:
They are an error-prone process whose properties and quality fluctuates significantly with environment, distance, and time.
Interference between different nodes and other technologies greatly impact the quality of links.
A MAC protocol needs to enable the following properties:
Collision-free communication.
Minimal overhearing of packets not destined to the node.
Minimal idling when no packets are arriving.
Minimal overhead and energy for organizing the transmissions.
Minimal delay and maximum throughput of packets.

## Slide 41: Summary (2)
There are several general approaches you can take:
Time division multiple access (TDMA) refers to a mechanism in which each node gets full control for some predefined amount of time (a slot). This is collision-free, but it suffers from large delays.
Carrier Sense Multiple Access (CSMA) refers to “first listen, then talk.” While the delay is low, the energy expenditure is high (the nodes never sleep) and it is not collision-free.
Duty cycling is the preferred way of organizing the sleep and awake cycles of sensor nodes. Sensor MAC, Berkeley MAC, and BoX MAC all work with duty cycling and are able to save considerable amounts of energy.
BoX MAC is based on B-MAC, but offers optimized communications for both unicast and broadcast transmissions, and is currently the preferred MAC protocol for sensor nodes. It does not need synchronization, has low delay, and low energy expenditure.