## Slide 1: INTRODUCTION TO WIRELESS SENSOR NETWORKS
CHAPTER 4: LINK MANAGEMENT
Anna Förster

## Slide 2: OVERVIEW
Introduction
Properties of Wireless Links
Error Control
Naming and Addressing
Link Estimation Protocols
  Link Quality Based
  Delivery Rate Based
  Passive and Active Estimators
Topology Control
  Centralized
  Distributed

## Slide 3: Introduction
Metrics for estimating quality of links:
Packet Reception Ratio (PRR)
Received Signal Strength Indicator (RSSI)
Link Quality Indicator (LQI)
Signal to Noise Ratio (SNR)
A wireless link is unreliable, not symmetric, and highly fluctuates in time and space.

## Slide 4: Links and Geographic Distance
Effective communication zone
Transitional communication zone
Clear communication zone

## Slide 5: Asymmetric Links

## Slide 6: Burstiness of Links
Measured with Conditional Probability Delivery Function (CPDF)

## Slide 7: Error Control
Guarantee communication to be:
Error-free
Loss-free
(In-sequence)
(Duplicate-free)

## Slide 8: Backward Error Control
Wait for the errors to happen and repair the problem:
Checksum or Cyclic Redundancy Checksum (CRC)
Automatic Repeat Request or Retransmit

## Slide 9: Forward Error Control (FEC)
Sending a new packet is very costly and uses not only energy, but also precious bandwidth. Sending a couple of more bits or bytes into a packet, which needs to get out anyway, is almost without cost.

## Slide 10: Forward Error Control (FEC)
Repeating Code
Problem: clustered errors

## Slide 11: Forward Error Control (FEC)
Interleaving Code

## Slide 12: Naming
Abstract Identification of Nodes
  A, B, C, etc.
  Mac Addresses of Devices
Role or data identification
  Washing Machine 1, Heating in the Living Room
  Temperature, humidity, light
Names can be unique or not

## Slide 13: Addressing
Reveals the position of the node
  In the network
  In the geographic world
Example: IP addresses

## Slide 14: Name and Address Assignment
Size and length: make sure you have enough addresses or names!
Storage: store in volatile or persistent memory
Positioning and Repositioning: change the name/address if the node moves or changes its role
Uniqueness: it is more practical to have unique names and addresses

## Slide 15: Link Estimation Protocols
Protocol which gathers link quality information about neighbors
Marks the neighbors as “good”, “average” and “bad”
Same as Neighborhood Management Protocol
Design criteria:
  Precision
  Agility
  Stability
  Efficiency

## Slide 16: Link Quality Based
Use RSSI or LQI (or similar or combinations thereof)
Example: all links with RSSI > -60 are considered very good links
Discussion of properties:
  Precision: not good
  Agility: rather good
  Stability: not good
  Efficiency: good for memory/communication overhead, average for processing needs

## Slide 17: Delivery Rate Based
Send many packets to all neighbors and estimate directly the delivery rate
Discussion of properties:
  Precision: quite good
  Agility: not good, depends on recalculation window
  Stability: good, opposite to agility, depends on recalculation window
  Efficiency: not good for memory/communication overhead, good for processing needs

## Slide 18: Passive and Active Estimators
Passive Snooping: Observe existing packets only
  Very efficient
  Not very precise or agile
Active Sending: Produce additional packets and observe their properties
  Very agile and precise
  Not efficient
Usually protocols are combination thereof

## Slide 19: Collection Tree Protocol (CTP)
CTP consists of a link estimator and a routing part.
Uses ETX: A network-wide metric, which computes how many hops on average a node needs to reach the sink
Defines a sending interval σlow to balance passive snooping and active sending
Another interval σlow is used to register changes in the network
Explores each neighbor in terms of its ETX to the sink
Sends regularly packets with own ETX to sink to all neighbors

## Slide 20: Topology Control
The topology (the neighborhood, the “visible” neighbors” can be controlled:
  Directly by changing the transmission power (saves energy)
  Indirectly by ignoring some neighbors with low quality (not often used)
Main Challenges:
  Asymmetric Links
  Directional Links
  Discovery of neighbors

## Slide 21: Centralized Topology Control
Gather all information about all nodes at the sink
Compute the optimal / desired topology and the corresponding parameters
Send the parameters to all nodes
Discussion:
  Very complex to obtain all data (link quality at different transmission powers)
  Not agile

## Slide 22: Distributed Topology Control
Each node tries out different transmission power
Each node observes the link quality to neighbors and decides on its own
Discussion:
  More flexible and situation-aware
  Very complex and might never stabilize

## Slide 23: Link Management: Summary
Quality is not linear with geographic distance.
Asymmetry exists, where quality is different in both directions.
Wireless links are bursty, i.e., bit errors occur not independently.
Link management involves several tasks:
Error control differentiates between forward error control and backward error control.
You assign unique names to individual nodes, which refer to their role or properties, and addresses, which refer to their positions.
Link estimation refers to maintaining quality indicators for individual neighbors. It can be delivery rate based or link quality based. Link estimation can be passive (overhear existing communication only) and active (creating its own communication). CTP uses a delivery rate based link estimator. Link estimation has to fulfill the following properties: precision, agility, stability, and efficiency.
Topology control plays with the transmission power of individual nodes to change their communication neighbors. It can be designed to be centralized (one node decides about the transmission power of all) or distributed (each node decides on its own).