## Slide 1: INTRODUCTION TO WIRELESS SENSOR NETWORKS
CHAPTER 5: MULTI-HOP COMMUNICATIONS
Anna Förster

## Slide 2: OVERVIEW
Routing Basics
Routing Metrics
Routing Protocols
  Full-network broadcast
  Location-based routing
  Directed Diffusion
  Collection Tree Protocol
  Zigbee

## Slide 3: Some Basic Definitions
Data source. The node in the network, which produces the required data and is able to send it out to other nodes in the network.
Data destination. The node in the network, which requires the
data and is able to receive it from other nodes in the network.
Data forwarder. Any node in the network, which is not the source or the destination of the data, which is able to receive it from another node and to send it further in the network.
Data sink. A dedicated node(s) in the network, which is the implicit destination of any data in this network.

## Slide 4: Communication Scenarios

## Slide 5: Routing
Routing is the process of selecting a sequence of nodes in the network, beginning from the data source(s) and ending at the data destination(s). This sequence of nodes is also called the routing path.
A valid routing path consists of a finite number of nodes and it does not contain loops.

## Slide 6: Metric: Location and Distance
Real geographic locations/distances
Approximations like Manhattan distance
Simple and clear
Costly to obtain locations and to exchange information (see Chapter 8)

## Slide 7: Metric: Hops
An approximation of distance in terms of communication
Not trivial to obtain for all nodes in the network
Reflects very well the topology of the network

## Slide 8: Metric: Number of Retransmissions (ETX)
An improvement of hops
Takes into consideration also the needed retransmissions
The number of retransmissions ETX over a route is always at least the number of hops over the same route.

## Slide 9: Metric: Delivery Delay
Delivery delay is the time elapsed between sending a packet at the source and receiving it at the destination, irrespective of the delay reason.
Reflects well the topology of the network and the interplay of different protocols and algorithms (e.g. TDMA schedules)

## Slide 10: Full-Network Broadcast
Flooding or full-network broadcast is defined as sending a single packet from any source in the network to all other nodes in the network, irrespective of whether they need this packet or not.
Main challenge: avoid broadcast storms

## Slide 11: Full Network Broadcast Algorithm

## Slide 12: Location-Based Routing
Any data forwarder (beginning at the source) compares the coordinates of the destination with the coordinates of all its neighbors and selects one to forward the data.
A neighbor is defined to have a positive progress towards some destination, when its own distance to the sink (independently from the routing metric used) is smaller than the distance to the sink of the current node.
If a routing process is always able to find a neighbour with positive progress towards the destination, it is guaranteed that the data packet will reach the destination in finite number of hops.

## Slide 13: Location-Based Routing: Deadends
In case of a deadend, follow “face routing” or the right-hand rule

## Slide 14: Location-Based Routing: Face Routing
The right-hand rule, and also the left-hand rule, is used to escape from a simply connected maze whose walls are connected to each other. Next time you enter a maze, put your right hand on the wall next to you and follow it. You are guaranteed to find another exit, if there is one.

## Slide 15: Location-Based Routing: Algorithm

## Slide 16: Directed Diffusion (DD)
A publish-subscribe algorithm
Sinks register with “information interests” to sensors
Sensors route data to all interested sinks
Based on delivery delay, but checked in both directions

## Slide 17: DD: Main Algorithm
Four phases
Makes sure that communication works in both directions (recall: asymmetric links! TDMA schedules!)

## Slide 18: DD: Variations
One Phase Pull: only Interest Dissemination and Fast Data Delivery
Push: Slow Delivery starts without Interest Dissemination

## Slide 19: Collection Tree Protocol (CTP)
Consists of Link Management (already discussed in Chapter 4) and Routing
Routing selects the neighbor with minimum ETX to sink:

## Slide 20: Zigbee
Node Roles:
  Coordinator
  Router
  End Device
Beacon-Less Zigbee:
  Routers use CSMA/CA, end devices sleep as much as they wish
Beacon-based Zigbee:
  Routers use TDMA to inform end devices when they are awake
  Requires time synchronization
Routing is based on AODV with full routing paths (Internet style vs. hop-by-hop in WSNs)

## Slide 21: Routing: Summary
Routing is the process of forwarding a packet from the source to a destination via intermediate nodes called routers or forwarders.
Routing in WSNs is performed always hop-by-hop.
You use routing metrics to decide which next hop to take: hops, delay, and ETX.
Routing highly depends on the MAC and link layer protocols at least.
Routing is very sensitive to link quality—the more stable links are, the better the routing protocol works.
Almost none of the currently existing protocols guarantee delivery of all packets. Instead, WSN routing is best effort.

## Slide 22: Routing: Summary of Protocols
Controlled full-network broadcast sends a single packet from one source to all other nodes of the network. It is guaranteed that it will stop once all nodes receive the packet.
Location-based routing selects next hops from a single source to a single destination by evaluating the geographic distance between the next hops and the final destination. Sometimes it enters a deadend, which needs to be solved via face routing.
Directed diffusion explores an alternative routing approach, where there are no real destinations for the packets but interests. Data is routed towards these interests and eventually arrive at the interested destination(s).
CTP (Collection Tree Protocol) is the most often protocol used in real- world applications. It builds a tree rooted at the sink and connects all nodes with the sink. The data gets collected from all nodes at the sink.
Zigbee is a (industrial) standard protocol that is less flexible than CTP.